## Slide 1: Network Neutrality
All internet traffic should be processed without differentation
  Origin
  Destination
  Content (outdated) - 5g slices/categories
Increasingly important as global debate intensifies and governments worldwide implement and withdraw regulations
Motivations for discriminatory traffic management
  ISP obtaining competitive edge
  Increase the number of customers and/or charge higher fees
Some traffic management pratices are considered to be “reasonable” and are allowed (should be transparent)
  Addressing ilegal content (piracy, spam or viroses)
  Prioritazing DNS queries
  Prioritize special services
Problem with detecting TD
  External observer with no access to network configurations
  Detect TD with only features of network(source,dst,port,etc)
  Identify which features trigger TD and where its happening

## Slide 2: 5g architecture and three main categories

## Slide 3: NWDAF
The Network Data Analytics Function (NWDAF) provides analytics information for different analytic events to NF consumers. It also allows NF consumers to subscribe/unsubscribe from notifications when an event is detected.
Main NF services provided by NWDAF:
  Nnwdaf_AnalyticsSubscription - Enables the consumer to subscribe/unsubscribe for network data analytics
  Nnwdaf_AnalyticsInfo - Enables the NF service consumers to request and get specific analytics from the NWDAF
  Nnwdaf_DataManagement - Enables the NF service consumers to subscribe/unsubscribe from notifications when subscribed event(s) are detected or retrieve the subscribed data from the NWDAF
  Nnwdaf_MLModelProvision - Enables the consumer to receive a notification when an ML model matching the subscription parameters becomes available
  Nnwdaf_MLModelInfo - Enables the consumer to request and get from NWDAF data containing MTLF ML Model Information
The first three services are provided by the Analytics logical function (AnLF) of NWDAF and the last two are provided by the Model Training logical (MTLF) function of NWDAF

## Slide 4: NWDAF Data Collection from NFs
The Data Collection from NFs is used by NWDAF to subscribe/unsubscribe at any 5GC NF to be notified for data on a set of events.
The Data Collection from NFs is based on the services of AMF, SMF, UDM, PCF, NRF:
  Event Exposure Service offered by each NF
  other NF services (e.g. Nnrf_NFDiscovery and Nnrf_NFManagement in NRF
Unified Data Management

## Slide 5: NWDAF API
  HTTP/2 messages
    HTTP headers
    JSON content
Example of the API URI of the Nnwdaf_EventsSubscription
{apiRoot}/nnwdaf-eventssubscription/v1/subscriptions
The request URIs used in each HTTP requests from the NF service consumer towards the NWDAF shall have the Resource URI structure as :
{apiRoot}/<apiName>/<apiVersion>/<apiSpecificResourceUriPart>

## Slide 6: NWDAF and data collection from data plane
NWDAF can get information from the data plane in two ways:
  Directly from UPF
  Indirectly through AF and other NFs
Important information NWDAF can get from the data plane:
  User data Congestion Analytics
    Throughput UL/DL
    Throughput UL/DL (peak) - Peak Throughput UL/DL over the measurement period.
    Timestamp - Time when measurements are taken.
    Measurement period
  Observed Service experience related network analytics
    Average packet delay and average loss rate

## Slide 7: NWDAF data collection from AF
AF acts as an interface between the UE and NWDAF
The AF communicates with the UE Application and collects data from UE Application
NWDAF gets information about UE from AF

## Slide 8: NWDAF and Charging information
CHF – Charging function and Nchf service interface
NF’s with CTF interact with CHF
SMF, AMF, SMSF and NEF support interactions with the CHF
Interactions done via Nchf interface
CTF (Charging trigger function)
CDR (Charging Data Record) – A structured collection of data that is utilized to compute billing. More than one CDR may be made if an event is lengthy or involves multiple costumers.

## Slide 9
Estrutura do Sistema

## Slide 10: QOS
Traffic Shaping
  Policing mechanism
  Avoids congestion on routers
  Controls packet bursts
Scheduling
  Garantees a minimum service rate
  Weighted fair queuing (R · wi /(Σwj) )
End-to-End QOS
  Charge directly for marked ACKs
  Indirectly by slowing down

## Slide 11: Multimedia Networking
Multimedia applications:
  Streaming stored audio/vídeo
    average throughput -> most important factor
    Interactivity - Dynamic Adaptive Streaming over HTTP (DASH)
    Continuous playout - (pre-fetching)
  Conversational voice/video-over-IP over UDP (delay)
    Real-Time Transport Protocol (RTP), streams of media
    Session Initiation Protocol (SIP), ASCII messages
  Streaming live audio/vídeo
Content distribution networks (CDNs) , clusters
Youtube HTTP streaming (private google CDN), no DASH (user selection), private google data centers
Netflix HTTP streaming (third-party CDNs, Amazon Servers)